## Slide 1: Cherry Philip v4 Build Instructions
By thegreatgunbantoad

## Slide 2: Kit contents
PET Tube
TP4056
LiPo Charger
Keystone
1043
Battery
Holder
Switch
DS18B20
Temp. Sensor
GY521 Accelerometer
BAT43 Diode
4k7 Resistor
220k Resistor
Wemos
D1 Mini
Cherry Philip v4 PCB

## Slide 3: Wemos D1 Mini
Keep the main board
Keep 2x 8 way board headers
Throw away the bottom 4 board sockets

## Slide 4: Prep: Accelerometer
The accelerometer comes with:
  GY521 Board
  8 way straight header
  8 way 90 degree angled header
Cut the 8 way angles header down to 4 way and solder as shown
Snip off the excess header section as shown
Keep the straight 8 way for the LiPo Charger

## Slide 5: Prep: LiPo Charger
Cut the 8 way header from the accelerometer into 6 off 1 way and 1 off 2 way, set the 2 way aside for later
Solder the 6 off 1 ways as shown

## Slide 6: Prep: Wemos D1 Mini
Solder the 2x 8 way board headers as shown
Program the board now, before it is soldered

## Slide 7: Prep: Battery holder
Snip the inside halves of the battery clips

## Slide 8: The Build: Quick Warning
Care must be taken during the build so as not to foul the battery when fitted in the holder, if the leads pierce the battery you risk a lithium fire
Ensure all joints are as flush as possible in the RED area, cut all legs flush to the board before soldering.

## Slide 9: The Build: 1: Accelerometer
Fit the prepped accelerometer as shown
Before soldering cut all legs flush to the PCB

## Slide 10: The Build: 2: Passives
Fit the 220k resistor
Fit the 4k7 resistor
Fit the BAS43 diode (take care that it is the correct way around)

## Slide 11: The Build: 3: Switch and Reset Header
Fit the Switch
Fit the 2 way header left over from the accelerometer

## Slide 12: The Build: 4: LiPo Charger
Fit prepped LiPo charger
Once fitted trim the pins down to prevent the shorting to the Wemos D1 Mini

## Slide 13: The Build: 5: Wemos D1 Mini
Fit the prepped and programmed Wemos D1 Mini
Don’t skip the programming before soldering it down, it USB connector gets difficult to get to

## Slide 14: The Build: 5: Temperature Sensor
Fit the DS18B20 temp. sensor
Before soldering cut all legs flush to the PCB

## Slide 15: The Build: 6: Battery Holder
Ensure all the solder joints on the board under the battery holder are as flush as they can be
Fit the prepped battery holder

## Slide 16: The Build: Complete